## Slide 1: Arthur H. Compton Lecture Series: An Intro to Climate Systems Engineering
Lecturer: Professor David Keith
October 4, 2025

## Slide 2
 | Speakers | Topics
Oct 4 | Keith | Introductions. Climate in 4 Dimensions. Emissions are peaking. Adaptation. Climate in Context.
Oct 11 | Archer | Carbon cycle and natural geochemical processes as basis to understand carbon removal.
Oct 18 | Shaw | Scientific basis for predicting climate changes in response to emissions of greenhouse gases and aerosol pollution.
Oct 25 | Cael | Carbon removal, including ocean alkalinity enhancement, land-based methods, bioenergy with carbon capture, and direct air capture with storage.
Nov 1 | Keith | Sunlight Reflection Methods (SRM) Part 1: How to Reflect Sunlight, the history of SRM, and why stratospheric sulfur aerosols are most plausible now.
Nov 8 | MacAyeal & Keith | MacAyeal on science of glaciers and interventions to prevent glacial melt. Keith on developing DAC technologies at Carbon Engineering, and lessons for cleantech.
Nov 15 | Shaw & Keith | The climate responses to SRM, potential side effects, and what can be learned from past aerosol pollution, highlighting the limits and uncertainties of experiments.
Nov 22 | Keith & Shaw | The future of climate systems engineering, and climate engineering in context.

## Slide 3: Outline
Reflecting sunlight, introduction
Why aerosol, why stratosphere, why sulfur?
Engineering
Comparing SRM methods
Climate response
Concerns

## Slide 4
Decarbonization
Sunlight reflection
Carbon removal
Economy
Emissions
Concentrations
Climatic change
Impacts
Adaptation
Decarbonization breaks the link between economy and emissions Ex: solar, nuclear, wind, carbon capture and storage…
Carbon removal breaks the link between historical emissions and climate change Ex: enhanced rock weathering, ocean alkalinity, direct air capture…
Sunlight reflection weakens the link between concentrations and climate change
Ex: stratospheric aerosols, marine cloud brightening, cirrus thinning…
Adaptation weakens the link between climate change and harm
Ex: solar air conditioning, climate-resilient agriculture, early warning…

## Slide 6: Why sulfuric acid aerosol is only plausible option for next few decades
SAI
Aircraft to deliver >0.3 Mt-S to >15 km exist today (e.g., 30 G650)
Multiple development pathways to 20 km alt aircraft
Very high confidence that sulfate aerosol are formed, have >1 year lifetime, and will cool Earth.
MCB
Significant uncertainty about cloud albedo response to additional CCN
No current development path to climate-relevant deployment tech.
CCT
Substantial uncertainty about cirrus cloud response to ice nuclei—easy to produce the wrong sign.
No current development path to deployable systems – but number of nuclei required is so low that there is a chance deployment tech is easer than MCB.
Space: no plausible deployment path in next two decades
Surface: no methods with > 0.5 Wm-2 and low environmental impact

## Slide 7: Why aerosol, why stratosphere, why sulfur?
Notes: Mikhail Budyko, a preeminent Russian climate scientist, was the first to propose spraying sulfur from airplanes to counteract global warming, calling it an “artificial volcano”. The year was 1974, a year marked (or marred) by bell-bottom jeans and the launch of Motorola’s 8080, the first successful general-purpose microprocessor. How can sulfur from airplanes still be the leading idea half a century later? Where is the innovation?

## Slide 8: Why aerosols?
Aerosol means any particle, solid or liquid, small enough to stay suspended in the air for a long time.
If particle that’s about as big as the wavelength of light, then it scatters light backwards about as efficiently as if were a tiny perfect mirror about ½ the diameter of the particle.
Particles are super efficient reflectors: a 0.5 µm particle scatters ~100× more light per unit mass than an everyday 50 µm mylar film.
Aerosol are the seeds from which clouds grow  tiny amounts of aerosol can have a big impact on cloud brightness and lifetime.
Incoming sunlight
Scattered sunlight

## Slide 9: Scattering from particles
For spherical homogenious particles one can compute scattering exactly using Mie theory given only:
Real index of refraction
Complex index (absorption)
Size parameter
K =
For r << λ
Scattered power proportional to r6
K proportional to r4
K proportional to λ-4
Volume-specific proportional to r3
For r > λ
K  2
Volume-specific proportional to r--1
Incoming sunlight
Scattered sunlight

## Slide 10
At 0.3 µm radius, 1 Tg of uniformly distributed sulfate aerosol has RF of 0.35 Wm-2.

## Slide 11: Visual impact of climate engineering that cools Earth ~ 1°C with aerosols
Clear Sky
Diamond
Sulfate
Lemon, Keith, and Albers, “Under a Not so White Sky: Visual Impacts of Stratospheric Aerosol Injection.” ERL, 2025

## Slide 12: Why the stratosphere?
Aerosols live about 100× longer in the stratosphere than in the troposphere (the lowest 90% of the atmosphere).
100× longer lifetime  100× less aerosols need to be added each year to reflect the same amount of sunlight.
Troposphere: Air is mixed by cycling thorough rain clouds roughly once a week.
Stratosphere: air is stratified, flow is laminar, and air can take years to cycle through.

## Slide 13: Injected aerosols are quickly distributed by strong zonal winds in stratosphere
Injection at 20 km altitude across range of latitudes (21 points @ 60N-S, 180E) for 1 month duration.
Key Takeaways:
Reasonable even global coverage after only a few months.
Localization is impossible for stratospheric aerosol injections.
Details: Lagrangian particles with settling. Wind data is high from high resolution reanalysis starting Jan 1, 2020. Hongwei Sun and Jim Franke

## Slide 14: Why sulfur?
The most common natural aerosol in the stratosphere.
Ocean plankton make Dimethyl sulfide (DMS) that is a major source of stratospheric sulfate aerosols.
These plankton are one of Lovelock’s Gaia feedback’s
Warming world  plankton make more DMS  more stratospheric aerosols  cooling
So, sulfate aerosol SRM is (arguably) a Nature Based Solution.
The environmental and climate impacts of sulfate aerosols have been studied in >10,000 scientific papers over a century. This deep knowledge greatly reduces chance of unknown unknowns.
Sulfur required for cooling is comparatively small:
(Mt-S/year)
Industrial emissions:
1980: 70 (peak global S pollution)
2025: 30
Pinatubo: 8
Global industrial sulfur market: 85
Amount needed to cool Earth 0.5 C: ~1.5

## Slide 15: Engineering

## Slide 16: Problem: copying volcanoes (SO2) does not work very well
Scattering gets much less effective when droplets are bigger than ~0.5 µm.
SO2 takes about a month to make condensable H2SO4
When a condensable gas is added slowly and evenly almost all of it ends up on existing droplets.
SO2 injection makes particles that are too to be effective
See: Hekendorn et al, The impact of geoengineering aerosols
on stratospheric temperature and ozone, ERL, 4 2009.

## Slide 17: Partial solution: add H2SO4 directly in a aircraft plume
Direct H2SO4 injection can make small particles with well controlled sized distribution.
 Much more effective.
Efficient formation of stratospheric aerosol for climate
Engineering by emission of condensable vapor from aircraft,
Pierce, Weisenstein, Heckendorn, Peter and Keith, GRL, 2010

## Slide 18
About 1 $/kg to the lower or middle stratosphere by several methods
Kilometers: | 12.2 | 18.2 | 21.3 | 24.4 | 30.5
Thousands of Feet (kft): | 40 | 60 | 70 | 80 | 100

## Slide 19
 | Mass/S | Toxic risk | Aerosol formation | Technical Uncertainties
SO2 | 2.0 | H | Weeks | Vaporization of droplets
H2S | 1.1 | H | Days to SO2 | Cost of production
S | 1.0 | L | SO2 is product | In situ combustion
CS2 | 1.2 | M | Half to OCS?  long lifetime | Vaporization or in-situ combustion, production cost
H2SO4 | 3.1 | M | Fast (sec)  accumulation mode aerosol | Minimal, vaporization
SO3 | 2.5 | H |  | Vaporization
Assume
SO2, H2S, and SO3 are carried as cold liquified gasses at 1 bar.
CS2, SO3, and H2SO4 are carried as liquids
Notes:  SO3 weeks
 SO2 (days)  SO3 weeks

## Slide 20: Sub-scale deployment
Assumptions:
Payload of 10,300 lb for Gulfstream G650 at 51,000 feet with 6,400 lb fuel sufficient for takeoff and climb (3,000 lb), diversion loiter and reserve (2,500 lb), and decent and landing (900 lb).
600 lb tankage and plumbing for carrying SO2 or H2S as chilled liquid at 1 bar.
Flight tempo: 6 sorties /day (roughly 1 hour per cycle), 330 operational days per year.
These assumptions yield ~ 10 ktons per aircraft per year to 15.5 km altitude.
10 modified business jets can put about 0.1 Mt-S/year into the mid-latitude stratosphere.
This is about the same as the background flow of S into the stratosphere.
Cooling of order 0.02 C or about 1 year of warming.
Solar geoengineering could start soon if it starts small Technology Review, 2024. Keith & Smith

## Slide 21: Comparing SRM methods

## Slide 22
Method | Confidence that substantial global RF (e.g. > 3 Wm-2) is achievable | Advantage | Disadvantage
Strat sulfates | Very high: Current technologies can likely be adapted to loft materials and disperse SO2 and relevant scales | Similarity to volcanic sulfate gives empirical basis for estimating efficacy and risks | Hard to adjust zonal distribution; ozone loss; stratospheric heating
Other strat aerosol | Moderate: depends on aerosol, lofting similar to sulfate but aerosol dispersal much more uncertain | Some solid aerosols may have less strat heating and minimal ozone loss | Hard to adjust zonal distribution; higher uncertainty than sulfates
Marine clouds | Uncertain: observations support wide range of CCN impact on albedo; significant work on development of spray systems, but no system-level analysis of cost of deployment | Ability to make local alterations of albedo; ability to albedo modulate on short timescales. | Only applicable on marine stratus covering ~10% of earth means RF inherently patchy; fast timescale raises termination risk
Cirrus | Uncertain: deep uncertainty about fraction of cirrus strongly depended on homogeneous nucleation; no studies of dispersal technologies nor system studies examining diffusion off CCN and link to flight profiles | Works on LW more than SW so could provide better compensation than “perfect” strat or space-based scatters; better RF uniformity that MCB | More ability to adjust zonal distribution that strat aerosols, perhaps less meridional adjustability.
Space based | Low physical uncertainty, but deep technological uncertainties about cost and feasibility | Possibility of near “perfect” alteration of solar constant. Spectral tailoring may be easier | Some methods (e.g. L1 point) would not allow zonal or meridional tailoring of RF
Solar geoengineering as part of an overall strategy for meeting the 1.5°C Paris target, MacMartin, Ricke, and Keith, Philosophical Transactions of the Royal Society, 2018

## Slide 23: Latham 1990

## Slide 26
Optical thickness is the natural log of the transmittance
Where transmittance is the fraction of light that is transmitted without any scattering or absorption
For a constant liquid water amount the optical thickness proportional to number to the 1/3:

## Slide 27
Credit: Brendan Kelaher, Southern Cross University
Notes: https://www.climaterepair.cam.ac.uk/events/bright-side-new-developments-marine-cloud-brightening-technology
Image Credit: Brendan Kelaher, Southern Cross University

## Slide 28
Credit: Sorooshian et al
Notes: Credit: Sorooshian et al

## Slide 29
Method | Confidence that substantial global RF (e.g. > 3 Wm-2) is achievable | Advantage | Disadvantage
Strat sulfates | Very high: Current technologies can likely be adapted to loft materials and disperse SO2 and relevant scales | Similarity to volcanic sulfate gives empirical basis for estimating efficacy and risks | Hard to adjust zonal distribution; ozone loss; stratospheric heating
Other strat aerosol | Moderate: depends on aerosol, lofting similar to sulfate but aerosol dispersal much more uncertain | Some solid aerosols may have less strat heating and minimal ozone loss | Hard to adjust zonal distribution; higher uncertainty than sulfates
Marine clouds | Uncertain: observations support wide range of CCN impact on albedo; significant work on development of spray systems, but no system-level analysis of cost of deployment | Ability to make local alterations of albedo; ability to albedo modulate on short timescales. | Only applicable on marine stratus covering ~10% of earth means RF inherently patchy; fast timescale raises termination risk
Cirrus | Uncertain: deep uncertainty about fraction of cirrus strongly depended on homogeneous nucleation; no studies of dispersal technologies nor system studies examining diffusion off CCN and link to flight profiles | Works on LW more than SW so could provide better compensation than “perfect” strat or space-based scatters; better RF uniformity that MCB | More ability to adjust zonal distribution that strat aerosols, perhaps less meridional adjustability.
Space based | Low physical uncertainty, but deep technological uncertainties about cost and feasibility | Possibility of near “perfect” alteration of solar constant. Spectral tailoring may be easier | Some methods (e.g. L1 point) would not allow zonal or meridional tailoring of RF
Solar geoengineering as part of an overall strategy for meeting the 1.5°C Paris target, MacMartin, Ricke, and Keith, Philosophical Transactions of the Royal Society, 2018

## Slide 30: Climate response

## Slide 31
No red symbols  None of the climate hazards is significantly exacerbated in any region
Moderated = move towards pre-industrial = less climate change ≈ better
Exacerbated = move away from pre-industrial = more climate change ≈ worse
Variable
Effect and statistical significance
Halving warming with idealized solar geoengineering moderates key climate hazards. Peter Irvine, Kerry Emanuel, Jie He, Larry W. Horowitz, Gabriel Vecchi, David Keith. Nature Climate Change, 2019.

## Slide 32
Halving warming with stratospheric aerosol geoengineering moderates policy-relevant climate hazards, Peter Irvine and David Keith. ERL, 2020.
For all the 4 regions where PE is exacerbated it is increasing P-E
 decreasing aridity
Same analysis method as prior but applied to GLENS (stratospheric aerosol geoengineering large ensemble Tilmes et al 2018) using CESM/WACCM.
With half-geoengineering computed by point-by-point linear scaling

## Slide 33: Concerns

## Slide 34
Towards constructive disagreement about geoengineering, David Keith. Science, 2021.

## Slide 35: Reliability of Solar Geoengineering Research
Ansatz: the reliability of a body of research increases with the duration of the research theme, the volume of research in the theme, the intellectual diversity of the research community, and the absence of commercial influence.
Examples:
New medical research shows how to extend lifespans: “Inhibition of IL-11 signaling extends mammalian healthspan and lifespan,” Nature, July 2024.
The standard model of quantum electrodynamic stands another test: “An improved bound on the electron’s electric dipole moment”, Science, July 2023.
Factors that suggest SRM research is unreliable:
Duration: most research done in the last decade
Intellectual diversity: much done by a small clique of researchers,
Volume: is low, in part because scientific research funding for SRM is well under 0.1% of total climate research.

## Slide 36: Reliability of Solar Geoengineering Research (2)
SRM is old: Research on SRM goes back to the early 60’s, it was reviewed in NAS reports of 1977, 1983, 1992. The first GCM simulation was published in 2000 by Bala and Ken. The long duration—albeit on a small scale and with little funding—means there has been time to find serious flaws, particularly given that climate researchers were generally biased against SRM research providing a solid motivation to root out errors.
SRM is better understood as an application of environmental geoscience than as an independent field: If research depended on new methods to study novel atmospheric processes, then the arguments for unreliability would carry more weight.

## Slide 37
Journal of the Atmospheric Sciences, 1961
Reliability of Solar Geoengineering Research (3)
Notes: https://journals.ametsoc.org/view/journals/atsc/18/1/1520-0469_1961_018_0081_sa_2_0_co_2.xml

## Slide 38: What’s the value of knowing more about SRM?
Reducing uncertainty about performance of SRM by a third in 2030 is worth roughly 4.5 $trillion
The value of information about solar geoengineering and the two-sided cost of bias. Tony Harding, Mariia Belaia, and David Keith. Climate Policy, 2022
Fine print: we compute net present value of optimal policy using a modified version of the Nordhaus DICE model with uncertainty in SRM and in climate sensitivity. Answer depends on many assumptions, but $trillion is right order of magnitude.
Big model full of approximations